RC Car WiFi Control System Documentation
- Adithyan.AS , B240382EE , NIT CALICUT

Overview

This project enables wireless, real-time control of a two-wheel drive RC car based on:
- ESP8266 as the WiFi-enabled controller,
- L293D motor driver for dual DC motors,
- External battery for motors,
- ROS2 as the software framework on the remote computer/controller,
- UDP protocol for fast, reliable communication.

Initially, MQTT was tried but dropped due to network issues; UDP was chosen for direct device-to-device packets.

System Block Diagram

[Gamepad or Joystick]
       │
    [Computer (ROS2)]
       │
   /----------\
   | WiFi |
   \----------/
       │
[ESP8266 NodeMCU]
   │ │
[L293D] [Onboard LED]
   │
[DC Motors, Battery]

Hardware Connections

WiFi & UDP Communication

- ESP8266 connects to your WiFi network (SSID & password set in code).
- In your controller/computer, ROS2 handles joystick/gamepad input and publishes to a topic (`/joy`).
- A Python ROS2 node (`rclpy`) subscribes to `/joy`, converts joystick axes to left/right PWM signals.
- The node sends these commands as simple comma-separated text (`left_pwm,right_pwm`, e.g., `120,-40`) via UDP to the ESP8266's IP and port.

ROS2 & ESP8266 Integration Flow

1. Joystick Input (On PC with ROS2):
Joysticks generate messages on `/joy`.

2. ROS2 Python Node:
Subscribes to `/joy`, translates values to PWM, sends UDP packets.

3. ESP8266 Firmware:
Receives UDP packets, parses PWM values, drives motors accordingly, updates LED and serial debug output.

 Why UDP Was Chosen Over MQTT

- MQTT requires a broker/server and may introduce latency or connectivity issues on local WiFi.
- UDP is direct, lightweight, and ideal for local real-time control.
- UDP works reliably on the same LAN without broker setup.

Example Usage & Workflow

1. Power On: ESP8266 connects to WiFi.
2. Launch ROS2 nodes: Start joystick and UDP sending nodes.
3. Control Car: Joystick inputs are sent as UDP messages to ESP8266.
4. Car moves: ESP8266 controls motors; onboard LED reflects movement status.

Troubleshooting Tips

- Ensure all grounds are connected together (ESP8266, L293D, battery).
- Use a separate power source for motors (stronger battery, not ESP power).
- Use serial debugging to verify UDP packets reception and PWM values.
- Check wiring carefully.

Detailed step by step procedure :

Step 1: Create a New ROS2 Python Package

Open a terminal on your ROS2 workspace (for example, `~/ros2_ws/src`).

Run the command to create a Python package:

bash:
cd ~/ros2_ws/src
ros2 pkg create --build-type ament_python joy_to_pwm_udp

This will create a folder called `joy_to_pwm_udp` with the basic package structure for Python.

Step 2: Place Your Python Code

Navigate to the newly created package folder:

bash:
cd joy_to_pwm_udp

Inside, create a `joy_to_pwm_udp` folder to hold your Python scripts:

bash:
mkdir joy_to_pwm_udp
```

Using your favorite editor, create a Python script named `joy_to_pwm_udp.py:

bash:
nano joy_to_pwm_udp/joy_to_pwm_udp.py

Paste your Python node code (from your earlier message with the UDP sending code) into this file.

import rclpy
from rclpy.node import Node
from sensor_msgs.msg import Joy
import socket

class JoyToPWM(Node):
    def __init__(self):
        super().__init__('joy_to_pwm_udp')

        self.declare_parameter("target_ip", "10.153.253.51") # ESP IP give the ip in which the node mcu is connected.
        self.declare_parameter("target_port", 4210)

        self.target_ip = self.get_parameter("target_ip").get_parameter_value().string_value
        self.target_port = self.get_parameter("target_port").get_parameter_value().integer_value

        self.get_logger().info(f"🌐 Target: {self.target_ip}:{self.target_port}")

        self.sock = socket.socket(socket.AF_INET, socket.SOCK_DGRAM)

        self.subscription = self.create_subscription(
        Joy,
        '/joy',
        self.joy_callback,
        10
        )
        self.get_logger().info("🎮 Subscribed to /joy")

    def joy_callback(self, msg):
        try:
        linear = msg.axes[1] # forward/backward
        angular = msg.axes[3] # turning

        self.get_logger().info(f"LINEAR: {linear} ANGULAR: {angular}")
        deadzone = 0.1

        if abs(linear) < deadzone: linear = 0.0
        if abs(angular) < deadzone: angular = 0.0
        left_pwm_raw = (linear + angular)
        right_pwm_raw = (linear - angular)

        # Clamp to [-1, 1]
        left_pwm_raw = max(-1.0 ,min(left_pwm_raw, 1.0))
        right_pwm_raw = max(-1.0 , min(right_pwm_raw, 1.0))

        # Convert to 0–255 PWM
        left_pwm = int((left_pwm_raw ) * 255)
        right_pwm = int((right_pwm_raw ) * 255)

        data = f"{left_pwm},{right_pwm}"
        self.sock.sendto(data.encode(), (self.target_ip, self.target_port))

        self.get_logger().info(f"📤 Sent PWM -> L: {left_pwm}, R: {right_pwm}")
        except Exception as e:
        self.get_logger().error(f"❌ joy_callback error: {e}")

def main(args=None):
    rclpy.init(args=args)
    node = JoyToPWM()
    try:
        rclpy.spin(node)
    except KeyboardInterrupt:
        node.get_logger().info("🛑 KeyboardInterrupt, shutting down.")
    finally:
        node.destroy_node()
        rclpy.shutdown()

if __name__ == '__main__':
    main()

Make sure the file starts with the correct ROS2 Python imports and your class `JoyToPWM`.

Save and exit.
Step 3: Edit ‘setup.py’ , ‘package.xml’ , ‘setup.cfg’

In the root of the package `joy_to_pwm_udp`, edit the `setup.py` file to make your script installable and executable by ROS2.

from setuptools import setup
import os
from glob import glob

package_name = 'joy_to_pwm_udp'

setup(
    name=package_name,
    version='0.0.0',
    packages=[package_name], # ensure there's an __init__.py in your package directory
    data_files=[
        ('share/ament_index/resource_index/packages', ['resource/' + package_name]),
        ('share/' + package_name, ['package.xml']),
        # If you have launch files, include them as well:
        *(
        [(os.path.join('share', package_name, 'launch'), glob('launch/*.launch.py'))]

        )
    ],
    install_requires=['setuptools'],
    zip_safe=True,
    maintainer='Your Name',
    maintainer_email='your.email@example.com',
    description='ROS2 node sending PWM commands via UDP from /joy topic',
    license='Apache License 2.0',
    tests_require=['pytest'],
    entry_points={
        'console_scripts': [
        'joy_to_pwm_udp = joy_to_pwm_udp.joy_to_pwm_udp:main',
       ],
       },

)

Package.xml :

  <?xml version="1.0"?>
<?xml-model href="http://download.ros.org/schema/package_format3.xsd" schematypens="http://www.w3.org/2001/XMLSchema"?>
<package format="3">
  <name>joy_to_pwm_udp</name>
  <version>0.0.0</version>
  <description>TODO: Package description</description>
  <maintainer email="user@todo.todo">user</maintainer>
  <license>TODO: License declaration</license>

  <buildtool_depend>ament_python</buildtool_depend>

  <exec_depend>rclpy</exec_depend>
  <exec_depend>sensor_msgs</exec_depend>

  <test_depend>ament_copyright</test_depend>
  <test_depend>ament_flake8</test_depend>
  <test_depend>ament_pep257</test_depend>
  <test_depend>python3-pytest</test_depend>

  <export>
    <build_type>ament_python</build_type>
  </export>
</package>

Setup.cfg:

[develop]
script-dir=$base/lib/joy_to_pwm_udp
[install]
install-scripts=$base/lib/joy_to_pwm_udp

Step 4: Add `__init__.py`

Inside the folder `joy_to_pwm_udp` (which holds your script), create an empty `__init__.py` file:

bash:
touch joy_to_pwm_udp/__init__.py

This lets Python treat it as a module.

Step 5: Build the Workspace

Go to your workspace root (`~/ros2_ws`) and run:

bash:
cd ~/ros2_ws
colcon build

After building, source the setup file:

bash
source install/setup.bash

Step 6: Run Your Node

Now you can run your UDP node with:

bash:
ros2 run joy_to_pwm_udp joy_to_pwm_udp

You should see the info messages about the UDP target IP and port, and it will subscribe to `/joy` topic to send UDP commands.

Bonus: Test the Joystick Node (if you want)

Make sure the `/joy` topic is being published by running:

bash:
ros2 topic echo /joy

Or run a joystick driver node (assuming you have a joystick connected and ROS2 Joy package installed):

bash
ros2 run joy joy_node

Your node receives `/joy` messages, converts them to PWM, and sends UDP packets to your ESP8266 motor controller.

Summary of Folder Structure

ros2_ws/
└── src/
    └── joy_to_pwm_udp/
        ├── setup.py
        └── joy_to_pwm_udp/
        ├── __init__.py
        └── joy_to_pwm_udp.py

Arduino code to be uploaded in node mcu :

#include <ESP8266WiFi.h>
#include <WiFiUdp.h>

const char* ssid = "name of ur wifi";
const char* password = "passsword";

WiFiUDP udp;
const int udpPort = 4210;
char incomingPacket[255];

// L239D Motor Driver pins
const int IN1 = D1; // GPIO14
const int IN2 = D2; // GPIO12
const int ENA = D5; // GPIO13
const int IN3 = D3; // GPIO5
const int IN4 = D4; // GPIO4
const int ENB = D7; // GPIO0

const int LED_BUILTIN_PIN = LED_BUILTIN; // GPIO2, onboard LED

// Blink control
unsigned long previousMillis = 0;
const long BLINK_INTERVAL = 500;
bool ledBlinkState = LOW;
enum LedMode { OFF, SOLID, BLINK };
LedMode ledMode = OFF;

void setup() {
  Serial.begin(115200);

  pinMode(IN1, OUTPUT); pinMode(IN2, OUTPUT); pinMode(ENA, OUTPUT);
  pinMode(IN3, OUTPUT); pinMode(IN4, OUTPUT); pinMode(ENB, OUTPUT);

  pinMode(LED_BUILTIN_PIN, OUTPUT);
  digitalWrite(LED_BUILTIN_PIN, HIGH); // Off (active low)

  stopMotorA();
  stopMotorB();

  WiFi.begin(ssid, password);
  Serial.print("Connecting to WiFi");
  while (WiFi.status() != WL_CONNECTED) {
    delay(500); Serial.print(".");
  }
  Serial.println("\nWiFi connected! IP: " + WiFi.localIP().toString());
  udp.begin(udpPort);
  Serial.printf("UDP Listening on port %d\n", udpPort);
}

void loop() {
  // LED management
  if (ledMode == SOLID) {
    digitalWrite(LED_BUILTIN_PIN, LOW); // Solid ON (active low)
  } else if (ledMode == BLINK) {
    unsigned long currentMillis = millis();
    if (currentMillis - previousMillis >= BLINK_INTERVAL) {
      previousMillis = currentMillis;
      ledBlinkState = !ledBlinkState;
      digitalWrite(LED_BUILTIN_PIN, ledBlinkState ? LOW : HIGH);
    }

  } else {
    digitalWrite(LED_BUILTIN_PIN, HIGH); // OFF
  }

  int packetSize = udp.parsePacket();
  if (packetSize) {
    int len = udp.read(incomingPacket, 255);
    incomingPacket[len] = '\0';

    int left_pwm = 0, right_pwm = 0;
    int parsed = sscanf(incomingPacket, "%d,%d", &left_pwm, &right_pwm);
    if (parsed == 2) {
      left_pwm = constrain(left_pwm, -255, 255);
      right_pwm = constrain(right_pwm, -255, 255);

      setMotorA(left_pwm); setMotorB(right_pwm);

      // Determine LED mode and serial messaging
      if (left_pwm > 0 && right_pwm > 0) {
        ledMode = SOLID;
        Serial.println("Forward");
      } else if (left_pwm < 0 && right_pwm < 0) {
        ledMode = SOLID;
        Serial.println("Backward");
      } else if ((left_pwm > 0 && right_pwm < 0) || (left_pwm < 0 && right_pwm > 0)) {
        ledMode = BLINK;
        if (left_pwm > 0)
        Serial.println("Right");
        else
        Serial.println("Left");
      } else if (left_pwm == 0 && right_pwm == 0) {
        ledMode = OFF;
        Serial.println("Stopped");
      } else {
        // Handles asymmetric zero (one stopped, one moving)
        ledMode = OFF;
        if (left_pwm != 0)
// Serial.println(left_pwm > 0 ? "Forward" : "Backward");
        Serial.println(left_pwm);
        Serial.println(right_pwm);
        if (right_pwm != 0)
        Serial.println(left_pwm);
        Serial.println(right_pwm);
// Serial.println(right_pwm > 0 ? "Forward" : "Backward");
      }
    }
  }
}

// Motor helpers
void setMotorA(int pwm) {
  if (pwm == 0) {
    stopMotorA();
  } else if (pwm > 0) {
    Serial.println("A");
    Serial.println(pwm);
    digitalWrite(IN1, HIGH); digitalWrite(IN2, LOW);
    analogWrite(ENA, pwm * 4); // 255 × 4 = 1020 (almost 1023)
  } else {
    Serial.println("A");
    Serial.println(pwm);
    digitalWrite(IN1, LOW); digitalWrite(IN2, HIGH);
    analogWrite(ENA, (-pwm) * 4);

  }
}

void setMotorB(int pwm) {
  if (pwm == 0) {
    stopMotorB();
  } else if (pwm > 0) {
    Serial.println("B");
    Serial.println(pwm);

    digitalWrite(IN3, HIGH); digitalWrite(IN4, LOW);
    analogWrite(ENB, pwm * 4);
  } else {
    Serial.println("B");
    Serial.println(pwm);
    digitalWrite(IN3, LOW); digitalWrite(IN4, HIGH);
    analogWrite(ENB, (-pwm) * 4);
  }
}
void stopMotorA() {
  digitalWrite(IN1, LOW); digitalWrite(IN2, LOW); analogWrite(ENA, 0);
}
void stopMotorB() {
  digitalWrite(IN3, LOW); digitalWrite(IN4, LOW); analogWrite(ENB, 0);
}

The purpose this documentation is to understand the execution of joy node in ros2 and udp communication protocol . For further details u can refer official ros2 humble documentation.
You should complete the tutorial of Ros2 from official site before doing this mini project.

You can’t follow the same steps for ESP32 ,there you should use microros commuication .

In the above method there is a flaw in the prototype I made , ie. while both pwm values become negative one of the motor stops , but it is an unsolvable issue as of now. You can think about that . All other directions are working properly if there is sufficient power supply.

*************